（Only suitable for TPS Series power supply）

Communication protocol (RS232 serial port):

*Communication settings: baud rate: 9600 (fixed), data bits: 8 bits, stop bits: 1 bit

*Communication data packet format：

| 1 frame of data contains a total of 18 bytes |
| --- |
| Start bit | 1Byte (fixed 0xAA) |
| Order bit | 1Byte |
| Data bit | 14Byte |
| Check Digit | 2Byte |
| Detailed explanation of frame data byte |
| Data byte | the data shows | Value |
| Data byte 1 | Start bit | 0xAA |
| Data byte 2 | Order bit | 0x01:control command 0x02:read back command |
| Data byte 3 | Set voltage high byte | Set voltage value*100/256 |
| Data byte 4 | Set voltage low byte | Set voltage value*100%256 |
| Data byte 5 | Set current high byte | Set current value*1000/256 |
| Data byte 6 | Set current low byte | Set current value*1000%256 |
| Data byte 7 | Set OVP high byte | Set OVP value*100/256 |
| Data byte 8 | Set OVP low byte | Set OVP value*100%256 |
| Data byte 9 | Set OCP high byte | Set OCP value*1000/256 |
| Data byte 10 | Set OCP low byte | Set OCP value*1000%256 |
| Data byte 11 | Read back voltage high byte | Read back voltage value*100/256 |
| Data byte 12 | Read back voltage low byte | Read back voltage value*100%256 |
| Data byte 13 | Read back current high byte | Read back current value*1000/256 |
| Data byte 14 | Read back current low byte | Readback current value*1000%256 |
| Data byte 15 | Output control byte | BIT7: output control BIT6: Independent output BIT5: Series output BIT4: Parallel output BIT3: reserved BIT2: reserved BIT1: Disarm the alarm BIT0: LOCK control |
| Data byte 16 | Working status byte | BIT7: CV status BIT6: CC status BIT5: OVP status BIT4: OCP status BIT3: OHP status BIT2: reserved BIT1: reserved BIT0: reserved |
| Data byte 17 | Checksum high byte | Accumulated sum of the first 16Byte/256 |
| Data byte 18 | Checksum low byte | Accumulated sum of the first 16Byte %256 |

*Communication process

The PC sends 1 frame of data to the power supply, a total of 18 bytes, the data is filled with the corresponding start bit, command bit, set voltage value, set Constant current value, OVP setting value, OCP setting value, output control byte and check byte.

After the power supply receives the data, it will verify the data. After the verification is qualified, the current power supply parameters will be set and the corresponding parameters will be backfilled. Return 18 bytes of data to the PC, and the PC can check the current status of the power supply through each byte of data in the data packet.